## Slide 1: Pal System Block Diagram
PIC
board
Motor
servo
Steer
servo
Pan
servo
Vs
Vs
Vs
27MHz
Receiver
antenna
Vs
Vs
GIO
GIO
GIO
US-TX
US-RX
Ultrasonic
Transmitter,
Omni-directional
Ultrasonic
Receiver,
Directional, Panning
MAX232
CS
GIO
GIO
SPI
3 SPI
ADC
RS232
Bluetooth
ICD2
MPLAB
ICD2
7.2V NiMH
7805
Vs
PWR
GIO
Remote/Autonomous
Vs
Pre-Amp
gain

## Slide 2: Pal Rover1 Board
ICSD
Str Thr Pan
dsp33FJ128GP802
Rcv
Trx
5V
3.3V
TLV2775

## Slide 3: Pal Timer Allocation
Timer 1: 40KHz Ultrasonic Signal
  Called every 12.5uS, each phase of sq wave
  Enabled by Timer 4, every 100mS
  Can Burst pulses, if desired
Timer 2: RC Servo Control
  20mS cycle, 3 channels, always on
Timer 3: ADC Acquisition Control
  50uS, for 50mS, gives 1000 data points.
Timer 4: Main Control Loop
  100mS, will be optimized later…
  Initiates Ultrasonic pulses
  Controls overall state machine